## Slide 1: Sheet 1
Microprocessors CMPS-201

## Slide 2: Today we will learn:
[x86] How to easily figure out the flags for any operation.
[x86] How the stack works.
[ARM] A few basics.

## Slide 3: x86 Flags
We have a number of status flags in the x86 flag register:
Carry Flag | Parity Flag | Auxiliary Flag | Zero Flag | Sign Flag | Overflow Flag
CF | PF | AF | ZF | SF | OF

## Slide 4: Carry Flag
Set when the operation results in a carry being generated.
Example: [AX = FF01].
  ADD AL, BL would result in a carry.
Example [AX = FFFF] and [BX = 0001]
  ADD AX, BX would also result in a carry.

## Slide 5: Parity Flag
This is set when the result , when converted to binary, has an even numbers of ones.
  Remember, zero is an even number.

## Slide 6: Auxiliary Flag
This is set when the first hexadecimal digit generates a carry.
AX = AB1F, BX = 0B01
  ADD AX, BX
    The first digits 1 + F = 10, a carry is generated, and AF = 1

## Slide 7: Zero Flag
Obviously, set when the result is zero.
This does not include the carry!
  FF + 1 = 00 and a carry of 1. This sets the zero flag.

## Slide 8: Sign Flag
Set when the result is negative.
AX = BA01
  ADD AL, AH = BA + 01 = BB
  When we convert 0xBB to binary: 0b1011_1011
  The MSB is 1. According to 2’s complement, this is negative. SF = 1.
BX = 0001
  ADD AX, BX = BA01 + 0001 = BA02. MSB = 1, SF = 1.

## Slide 9: Sign Flag: Hack
A quick way to check if a number is negative:
  Is the left most digit an 8 or more?
    Then, It is negative.
8 in binary = 0b1000, the MSB is one.

## Slide 10: Overflow Flag
Set if the result is an invalid 2’s complement.
If we add two positive numbers and the result is negative:
  This is an overflow.
If we Add two negative numbers and the result is positive:
  This is called underflow, but gets the same treatment as an overflow.
Both cases set the overflow flag.

## Slide 11: The Stack
The stack pointer SP is a 16 bit register.
It always points to the top of the stack.
We can push 16 bit values only. (Can’t PUSH AL, for example).

## Slide 12: Pushing onto the Stack
The SP decrements by 2 (why not 1?)
Since the memory is byte addressable (it is 8 bits wide), We need two places to store a 16-bit register.
Little Endian ! The lower part of the register is written into the lower part of the memory, and the higher part is written in the higher part of memory.

## Slide 13: Popping from the Stack
The reverse of pushing.
The lower part of the memory is written in the lower part of the register, and the higher part of the memory is written in the higher part of the register.
The SP increments by two.

## Slide 14: Any questions?
“There are no foolish questions and no man becomes a fool until he has stopped asking questions.” – Charles Proteus Steinmetz

## Slide 15: Thank you.